## Slide 1
B.TECH FINAL YEAR PROJECT · RAMDEOBABA UNIVERSITY, NAGPUR
Smart Road Hazard
Detection System
Real-time pothole & speedbreaker detection using ESP32 + ultrasonic sensor, crowd-verified across 3 independent vehicle detections, shown live on an interactive map — no app install required.
Krish Potanwar · Soumya Jaiswal · Bhavika Valecha · Shubhiksha Bisen · Harshit Widhwani
smart-road-hazard.vercel.app
github.com/Krishpotanwar/SmartRoadHazard
wokwi.com/projects/458668521911516161
ESP32 + HC-SR04
Flask REST API
Firebase RTDB
Leaflet.js
Vercel + Render

## Slide 2
THE PROBLEM
India's roads are breaking things
India has over 6 lakh kilometres of roads. Potholes cause thousands of casualties every year. Most hazards go unreported for months — the detection gap is the real problem.
~3,000
pothole-related deaths per year (NCRB)
25,000+
road injuries annually from bad roads
months
average time a hazard sits before repair
By the time someone opens a reporting app and files a hazard, the next hundred vehicles have already hit the same hole. Manual reporting cannot keep pace.

## Slide 3
EXISTING SOLUTIONS
Three approaches, three limitations
None verify a hazard across independent sources before alerting.
Approach
How it works
The gap
Manual apps (Pothole Ratha, etc.)
User photographs and submits the hazard
Needs a human to notice, stop, and act — zero automation
Phone accelerometer methods
Phone IMU detects a sudden bump while driving
Speed bumps, rail crossings, and rough braking all trigger false alerts
Municipal road surveys
Inspection crews drive marked routes periodically
A new pothole today won't appear in surveys for weeks
Smart Road Hazard (this project)
Ultrasonic sensor on each vehicle; Flask verification; live map
Automated, continuous, depth-graded, verified before any alert fires

## Slide 4
SYSTEM OVERVIEW
From sensor to screen in under 2 seconds
Five layers, each with a single job. The crowd-verification middle layer is what keeps false alerts out.
HARDWARE
ESP32 + HC-SR04
Reads road surface distance at 10 Hz
→
CLASSIFY
Depth grading
Deep / Medium / Shallow / Speedbreaker
→
VERIFY
Crowd logic
3 detections within 15 m → confirmed
→
SYNC
Firebase RTDB
Instant push to all connected clients
→
DISPLAY
Leaflet map
Color-coded markers + alert bar
Flask REST API
Firebase RTDB
Leaflet.js + OSM
ESP32 C++
SQLite
Vercel + Render
Wokwi sim

## Slide 5
WHAT MAKES IT DIFFERENT
Three decisions that actually matter
01
Depth classification
The sensor measures how far the road surface drops against a rolling 10-reading baseline. Delta above 25 cm = deep pothole. 8-15 cm = speedbreaker. Objective depth — not a user guess. Why it matters: repairs can be prioritised by severity, not just location.
02
Crowd verification
A hazard only gets published after 3 independent vehicles detect it within a 15-metre radius (Haversine formula). One vehicle hitting a bump does not trigger alerts. Three independent detections does. The system self-validates. Why it matters: alert fatigue is why drivers stop trusting hazard apps.
03
Shadow alerts
When a medium or deep pothole is verified, the dashboard fires a warning banner that auto-dismisses in 5 seconds. Specifically helps drivers behind trucks and buses who cannot see the road surface ahead of them. Why it matters: the most dangerous potholes are the ones you can't see coming.

## Slide 6
HARDWARE LAYER
The sensor setup
Simulated entirely in Wokwi. Same firmware would run on a real vehicle mount. No physical hardware needed to run, test, or demo the system.
Components
• ESP32 microcontroller
• HC-SR04 ultrasonic sensor
• SSD1306 OLED display
• 3 status LEDs (Red / Green / Blue)
Trigger: GPIO 5 · Echo: GPIO 18 Baseline: average of first 10 readings. All subsequent readings are deltas against that baseline.
Classification logic
delta > 25 cm → DEEP POTHOLE
delta 15 – 25 cm → MEDIUM POTHOLE
delta 5 – 15 cm → SHALLOW POTHOLE
delta −5 to −15 → SPEED BREAKER
| delta | < 5 cm → CLEAR ROAD
Serial output: "POTHOLE,DEEP,21.1458,79.0882"
Deep pothole
Medium pothole
Shallow pothole
Speed breaker
Unverified

## Slide 7
BACKEND
Where the verification logic lives
Three Python files. The crowd-verification inside database.py is the core of the whole system.
bridge.py
Reads serial output from ESP32 (or generates realistic Nagpur route data in demo mode). Pushes detections to the Flask API and Firebase simultaneously.
database.py
Every new detection calls add_detection(). It checks existing records within 15 m using Haversine. If the count hits 3, the 'verified' flag flips to 1 and the alert becomes active. That is the entire algorithm.
server.py
Flask REST API — 5 endpoints, full CORS enabled. GET /api/hazards — verified hazards only POST /api/hazards — submit a new detection Deployed: Render · Port 5001
# Verification logic (simplified) nearby = db.query('SELECT * FROM hazards') matches = [h for h in nearby if haversine(h, new) < 15] if len(matches) >= 3: mark_verified(hazard_id) # alert fires

## Slide 8
FRONTEND
The live map dashboard
Runs entirely in the browser. No app install. No API key. No billing account. Leaflet.js on OpenStreetMap — free, fast, deployable on Vercel in under a minute.
What the map shows
Grey
1-2 detections — not yet confirmed
Yellow
Shallow pothole (verified)
Orange
Medium pothole — shadow alert fires
Red
Deep pothole — highest priority alert
Blue
Speed breaker
Live sync
Firebase listener mode keeps all open browser tabs updated in real time. Local mode polls the API every 2 seconds as a fallback.
Shadow alert bar
Warning banner slides in when a medium or deep hazard is verified. Auto-dismisses in 5 seconds — enough time to slow down, not enough to annoy.
Tooltip detail
Hover any marker: type, severity, and verification progress (e.g. '2/3 verified' or '✓ Verified').
No API keys
Switched from Google Maps (requires billing) to Leaflet.js + OpenStreetMap. Free, no account, deployable by anyone with zero setup.

## Slide 9
DEMO WALKTHROUGH
Running it yourself
Two paths: Wokwi (full end-to-end) or keyboard simulator (faster for live demos).
1
Open Wokwi simulation at wokwi.com/projects/458668521911516161 and drag the HC-SR04 distance slider to trigger detections.
2
Open the live dashboard at smart-road-hazard.vercel.app in a second tab.
3
Trigger the same location 3 times — watch the grey pin change colour and the shadow alert bar appear at the bottom of the screen.
4
Alternatively: run python simulator.py locally and press 1 (deep pothole) or 4 (speedbreaker) to inject test detections via keyboard.
# Local demo — no hardware needed cd backend && python server.py python bridge.py --demo # auto-generates Nagpur route data # open frontend/index.html in browser

## Slide 10
RESULTS & METRICS
What the system delivers
These are engineering parameters, not marketing claims. Every number is a deliberate design choice that can be tuned.
2 sec
Map update latency (polling interval)
15 m
Crowd verification radius (Haversine formula)
3
Independent detections required before any alert fires
4 types
Deep / Medium / Shallow / Speedbreaker
5 cm
Minimum distance delta that registers as a hazard
0
External API keys or billing accounts required

## Slide 11
CHALLENGES
Three walls we actually hit
None of these were theoretical. Each one blocked progress and needed a real fix.
macOS blocked port 5000
AirPlay Receiver on macOS Monterey silently occupies port 5000 — Flask's default. The app would start, appear to work, then randomly fail. Moved to port 5001. Lesson: when something works in CI and fails on a dev machine, check what else is listening on that port.
Google Maps requires billing
The original design used Google Maps. Midway through, billing became mandatory even for free-tier usage. Switched to Leaflet.js + OpenStreetMap — no key, no account, no surprises. Also made the project deployable by anyone with zero setup.
Wokwi serial output too fast to demo
When the simulation runs at full speed, serial data floods the bridge faster than a live demo can follow. Built simulator.py — keyboard-driven, press 1-4 to fire specific hazard types on demand. Better than real hardware for presentations.

## Slide 12
WHAT COMES NEXT
From simulation to road
The gap between 'working demo' and 'deployed on real vehicles' is two steps: real GPS hardware and an actual road test in Nagpur.
NEXT 2 WEEKS
Replace simulated GPS with a NEO-6M real GPS module on physical ESP32 hardware
Switch from 2-second polling to WebSocket push for sub-second map updates
Road test: mount sensor on a bicycle, run on Nagpur streets, compare to simulation
NEXT 1 – 3 MONTHS
React Native / Flutter mobile app — detection on-device, no ESP32 needed for consumer use
Fleet management view: all vehicle positions + hazards on one screen
RESEARCH DIRECTION (AI / ML ALIGNMENT)
Camera + YOLO object detection to visually confirm potholes alongside ultrasonic data
Push verified hazards to NHAI or Smart City municipal APIs automatically

## Slide 13
CONCLUSION
What we built, and why it works
Most road hazard systems either need a human to file a report, or accept every sensor reading as ground truth. This system does neither. It collects sensor data automatically and only acts when three independent vehicles agree on the same hazard within 15 metres. That one design decision — crowd verification before alerting — is what keeps it usable on real roads.
Depth classification
Objective severity grading from sensor data, not user judgment
Crowd verification
Three independent detections before any alert reaches a driver
Shadow alerts
Real-time warnings for drivers who cannot see the road ahead
smart-road-hazard.vercel.app
github.com/Krishpotanwar/SmartRoadHazard
B.Tech CSE (AI & ML) · Ramdeobaba University, Nagpur · 2024 – 25
Thank you